## What does the storage of Hazardous Chemicals Regulations require?

## The Work Health and Safety Act 2011 and Regulation (WHS) require you to store hazardous chemicals (pesticides, fuel, diesel and other chemicals) safely on your farm, keep them secure and keep a record (register) of all hazardous chemicals stored.

## Information on how to safely store agricultural chemicals (including pesticides and fuels) can be found in:

## The safe use and storage of chemicals in agriculture NSW Code of Practice 2006

## Managing risks of hazardous chemicals in the workplace Code of Practice July 2014

## Australian Standard AS 1940: 2004 The storage and handling of flammable and combustible liquids

## Australian Standard AS 2507:1998 - the storage and handling of agricultural and veterinary chemicals.

## Who does the law apply to?

The law applies to all farm businesses.

## Do you have to record my own household chemical use?

No. You do not need to make a record when you use or store pesticides around your own home or garden.

## What is a hazardous chemical?

Most (nearly all) pesticides (including herbicides, fungicides, insecticides, fumigants, bactericides, rodenticides, baits, lures, repellents and pesticides used on animals to control external parasites), fuels (diesel, ULP, kerosene, Avgas, Avtur) and industrial chemicals (solvents, sanitisers and disinfectants) are hazardous chemicals and need to be stored safely.

## How do I store agricultural chemicals and hazardous chemicals safely?

## How much to be stored? Work out what the maximum quantity and size of packaging you are going to store on farm; (20 L drums, EnviroDrums, 1,000 L IBC (shuttles).  This forms the basis of the size and bunding to store and contain spills.  The greater amount of pesticide stored the larger the hazard and more controls will need to be put in place. Where possible reducing the quantity of chemicals stored is the most cost effective way of reducing risk and minimises chemical container disposal.

## Consider location and design of the chemical storage area:

## Chemical stores need to be located away from:

## Property boundary, homes and workshops and ignition sources

## Environmentally sensitive areas; rivers, creeks, natural water ways

## Separate building or segregated enclosure

## Secure - to keep unauthorised people out

## An impervious floor – i.e. cement

## Ventilated – cross flow ventilation to stop the build up of fumes

## Well lit - so you can see what’s stored and read labels

## Bunded with or without a sump - to contain spills

## Emergency Shower and Eye Wash Station

## The following emergency equipment must be available:

## A suitable fire extinguisher -

## First Aid kit - with a Portable Eye Wash, at least 250 mL Eye Wash bottle. Common injuries are eyes and crush injury from spills, stacking and falling drums and pallets

## Emergency Spill Recovery Kit - to cleanup spills

## An Emergency Response Plan - to remind workers what to do in an emergency and important contact numbers (e.g. Poisons Information Centre)

## An Emergency Eye Wash Station and Emergency Shower freely accessible in or adjacent the store

## Signage - to remind people what to do and what’s in the store

## You are required to separate hazardous chemical groups e.g. Poisons, Flammable, Oxidising products.

## It is also good practice to separate herbicides, insecticides, fungicides and other groups so they are not mixed up and accidentally misused.

## What is a bund and how big does it have to be?

## A bund is a wall surrounding a chemical store that will contain chemical spills.

## Spill containment may be:

## a sloping floor (with or without a sump, holding pit or tank) with a bund

## trenches or spoon drains, or a combination of the above

## For ‘minor’ farm chemical stores, the bund should contain 100% of the largest container and/or 25% of the total volume stored, which ever is the greater.

## All above ground bulk tanks must have a form of spillage control (e.g. bunding). Bunding for bulk tanks under a roof must contain 100 per cent of the largest container, or 110 per cent for outside tanks (to allow for possible rain). A bulk tank includes bulk transport containers such as IBC (Intermediate Bulk Container).

## A sump will help drain and contain spills.  The volume of the sump can be included in the volume of the bund; a sump will help clean up spills and water.

## There are many different floor designs, including sloping floors to the rear and middle of the shed with or without a sump; flat floors with a drive over hump for fork lifts and vehicles to easily load and unload drums, pallets and IBC (shuttles).

## The chemical store may also incorporate a loading pad; consideration and planning is required to containing runoff in a drainage/evaporation pit.

## What is an Emergency Spill Recovery Kit?

## An emergency spill kit is:

## a recovery drum large enough to contain the largest container (to put leaking drums in)

## funnel and decanting tap or siphon pump

## hydrated lime or soda ash (to decontaminate spills)

## sand, soil or other chemical absorbent (to help cleanup spills)

## a shovel and broom, and

## PPE e.g. gloves, apron, eye protection to use when cleaning up spills

#### Safety Signs

## The following signs are required on the outside all chemical sheds that store pesticides on farms. Prohibition signs (white, black, red signs) indicate an action or activity is not permitted.

## Emergency signs: these signs indicate the location of, or directions to emergency related facilities.

## Fire Extinguisher

## First Aid kit, and

## Emergency Eye Wash/ Shower

## Spill Kit

## What records do I keep?

Work health and Safety Regulation (2011) requires a record to be kept of all quantities of Hazardous Chemicals stored on the farm.

This is your Pesticide Register and where required when you exceed the quantities of Hazardous Chemicals stored, becomes your Chemical Manifest. It is essential to make a list of pesticides stored on farm and refer to the Safety Data sheet for hazards associated with each chemical product

- See Appendix 1 – Pesticide Register

- See Appendix 2 -  Hazardous Chemical Manifest (records the name and quantity of the products stored, and Dangerous Goods (Hazardous Chemical) Category of each product.

## Is my chemical store a ‘Minor’ storage facility?

## Most cotton farm pesticide stores would be classified as minor stores according to the Australian Standard AS 2507 – 1998. Most farms will have quantities and types of chemical that will not exceed this classification. This needs to be determined by developing a pesticide register or hazardous chemical manifest. When quantities exceed 1000kg or Litres combined, there are additional specifications which must be met and complied with.

#### Placards for hazardous chemicals

Placard Quantities - describes the threshold quantities where signage is required to identify products stored.(See table 1.1 for quantities)

If hazardous chemicals on farm exceed placard quantities the following Dangerous Goods diamonds are placed outside the chemical store.

The most common signs needed may be

Ensure you check the product labels/ Safety Data Sheet in the chemical store for the correct signage. The signs must have sides of at least 100mm long.

#### Outer Warning Placarding

#### When the Placarding Quantity is exceeded, the following HAZCHEM sign is placed on the outside of the chemical store or property entrance. (See table 1.1 for quantities).

The word HAZCHEM must be in red lettering, not less than 100 mm high, on a white or silver background.

The purpose of the sign is to let emergency services personnel know this chemical shed is storing Hazardous Chemicals in significiant quantities and what to expect if an emeregnecy occurs.

#### What is a Hazardous Chemical Manifest?

When chemical products stored exceed Manifest Quantities (see table for thresholds) a Hazardous Chemical Manifest needs to be developed.

The Hazardous Chemical Manifest will inform emergency services of the location, hazard category and quantities of hazardous chemicals stored on farm.

Table 1.1 Hazardous Chemicals – Placard and Manifest Quantities (WHS Regulation 2011 (schedule 11)

| Description – Hazard Class | Hazard Category | Placard Quantity | Manifest Quantity | ADG Code |
| --- | --- | --- | --- | --- |
| Acute Toxicity | Category 1 | 50 L/ kg | 500 L | 6.1 (PG I) |
|  | Category 2 | 250 L/ kg | 2,500 L | 6.1 (PG II) |
|  | Category 3 | 1,000 L/ kg | 10,000 L | 6.1 (PG III) |
| Flammable Liquids | Category 1 | 50L | 500L | 3 (PG I) |
|  | Category 2 | 250L | 2,500L | 3 (PG II) |
|  | Category 3 | 1,000L | 10,000L | 3 (PG III) |
|  | Category 4 | 10,000L | 100,000L | C1 – combustible liquid |

Reference: Extract from Code of Practice – Managing the Risks of Hazardous Chemicals in the Workplace - Appendix D:  Placard and Manifest Quantities of hazardous chemicals.

If manifest quantities exceed the quantities specified in the legislation (WHS Reg – Schedule 11), then you must notify:

- Notify the agency in your State:

SafeWork NSW – Hazardous Chemicals Notification http://www.safework.nsw.gov.au/licences-and-registrations/notifications-and-permits/dangerous-goods-notifications

WorkCover QLD – Hazardous chemical notification https://www.worksafe.qld.gov.au/injury-prevention-safety/hazardous-chemicals/notifications-for-hazardous-chemicals

- Develop a Hazardous Chemical Manifest

- Develop a site plan (mud map) of where the store is located on the property.

- Lodge an emergency plan to:

  - Fire and Rescue NSW http://www.fire.nsw.gov.au/page.php?id=9033

  - Queensland Fire and Rescue Service https://www.fire.qld.gov.au/planning/

This site plan and manifest is only available to Emergency Services personnel in an Emergency. Notification is crucial to the provision of an effective emergency response by emergency departments.

#### HAZCHEM Signs and Dangerous Goods Codes

The HAZCHEM Code provides information for emergency services in the event of a leak, spill or fire.

- The Fist Numeral - describes what type of fire agent to use.

- The Second letter - describes the protective equipment to use, and

- The Third Letter - wether to consider evacuation of the site.

Consider this HAZCHEM sign used for the transport and storage of anhydrous ammonia.

The HAZCHEM Code 2RE specifies

2 - Use a fog for a fire or a spill

R - Use full body protective clothing with Breathing Apparatus, and

E - Consider Evacuation of the site.

While the Hazchem diamond provides health warning that that is a Toxic Gas and that it is also Corrosive.

PROPERTY NAME & ADDRESS:

PHONE:  		FAX:

| Product Name | Company | Active | Pack Size | Quantity (L or kg) |
| --- | --- | --- | --- | --- |
| Roundup CT | Monsanto | glyphosate | 20 L | 48 |
| Spray Seed | Syngenta | paraquat and diquat | 20 L | 60 |
| Roundup Ready Flex | Monsanto | Glyphosate | 1,000 L | 2,000 L |
| SpraySeed |  | Paraquat and diquat | 1,000 L | 4,000 L |
| and so on |  |  |  |  |

PROPERTY NAME & ADDRESS:

PHONE:  		FAX:

| Product Name | Active | Pack Size | Quantity (L or kg) | ADG | Hazard Class | PG | Sub Class | Poison Schedule | UN Number | Where Stored | Current SDS Date |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Roundup 720 | glyphosate | 1,000 L IBC | 12,000 | No |  |  |  | S5 | 3082 | Chemical Shed |  |
| Spray Seed | paraquat and diquat | 20 L | 60 | Yes | 6.1 | III |  | S7 | 3016 | Chemical Shed |  |
| Roundup Ready Flex | glyphosate | 1,000 L IBC | 2,000 | No |  |  |  | S5 |  | Chemical Shed |  |
| Rogor | dimethoate | 20 L | 15 | Yes | 6.1 | III | 3 | S6 | 3017 | Chemical Shed |  |
| Diuron 500 SC | diuron | 40 L | 120 | No |  |  |  | Nil |  | Chemical Shed |  |
| Dropp UltraMAX | thidiazuron +diuron | 160L | 400 | Yes | 9 | III |  | Nil | 3082 | Chemical Shed |  |
| Prep 720 | ethephon | 20 L | 80 | Yes | 8 | III |  | S6 | 3265 | Chemical Shed |  |
| Liberty | glufosinate ammonium +trifloxystrobin | 20 L | 40 | No |  |  |  | S5 |  | Chemical Shed |  |
| Movento 240 SC | spirotetramat | 20 L | 60 | Yes | 9 | III |  | S6 | 3082 | Chemical Shed |  |

| Product Name | Active | Pack Size | Quantity (L or kg) | ADG | Hazard Class | PG | Sub Class | Poison Schedule | UN Number | Where Stored | Current SDS Date |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Nufarm Amicide 625 | 2, 4 D amine | 20 L | 1,200 | No |  |  |  | S6 |  | Herbicide Shed |  |
| Confidor 200 SC | Imidicloprid + prochloraz | 20 L | 85 | No |  |  |  | S5 |  | Herbicide Shed |  |
| Atrazine 900 WG | atrazine | 20 L | 220 | No |  |  |  | S5 | 3077 | Herbicide Shed |  |
| eChem Chlorsulfuron 750 WG | chlorsulfuron | 500 g | 2.5 kg | No |  |  |  | S5 |  | Herbicide Shed |  |
| Ally | metsulfuron | 500 g | 10 kg | No |  |  |  | Nil |  | Herbicide Shed |  |
| Farmoz Clincher Plus | metolachlor | 1000 L | 400 | CI | 3 | IIII |  | S5 |  | Herbicide Shed |  |
| Verdict | haloxyfop | 20 L | 40 | No |  |  |  | S6 |  | Herbicide Shed |  |
| Garlon | triclopyr | 20 L | 25 | No |  |  |  | S6 | 3082 | Herbicide Shed |  |
| Tordon 2,4,2 | MCPA + picloram | 20 L | 140 | No |  |  |  | S5 |  | Herbicide Shed |  |
| Starane | fluroxypyr-meptyl | 20 L | 200 | No |  |  |  | S5 |  | Herbicide Shed |  |
| Boxer Gold | prosulfocarb + S-metalochlor | 20 L | 20 | No | C1 |  |  | S6 |  | Herbicide Shed |  |