FARM HEALTH AND SAFETY

WE SHARE RESPONSIBILITY

SAFETY INDUCTION INFORMATION

FOR GRAIN HARVESTING

The health and safety of all the people working on farms, especially during harvest is the most important responsibility that we all share.

As owner / manager/ contractors, we have responsibility for the health and safety of workers and others working.

The following are practical working practices and arrangements that we see as important for ensuring the health and safety of all workers and contractors.

Please read this leaflet carefully, and if you do not understand any section, please ask for an explanation.  As a contractor, we ask you to include this information in the information that you give to all workers in your team.

# REPORTING HAZARDS

We have already made a check of this farm and machinery to identify hazards for workers and others, and we are working to continue preventing injury and illness.

We ask that you report hazards that you notice to the owner/ manager, and we will welcome your suggestions for how to reduce the risk of injury/ illness.

# HAZARDS ON THE FARM

Attached is a farm map.  Marked on the farm map you will find hazards that we have identified, that may affect the work that you do on the farm, or may be particularly hazardous to your operation.  These include:

Powerlines

Washaways/ Creeks/ Dams / Boggy or wet areas

Recently sprayed areas or proposed spray activity that may affect your work on this farm

Other

# ACCESS TO AREAS OF THE FARM

The tracks and roads on this farm are not made to public road standards.  Vehicle speed should not exceed …………………………….km/h.  When driving near buildings, reduce speed so that you can stop quickly to prevent collision or runover and avoid injury to others.

The attached farm map outlines access roads and areas of this farm to which you and your workers will have access.

# WORK CLOTHES

Your workers are expected to come to work dressed in suitable clothes, which do not pose a safety risk.  These include:

Suitable work boots with non-slip soles for work on the farm.

Work overalls, trousers or sensible work shorts.

Long sleeved shirt (preferably), buttoned at the wrist, or rolled up in such a way that no loose ends can be caught in machinery or on protruding materials.

Shirts tucked into trousers, and no loose clothing that could be caught in machinery, including corks of jackets etc.

A wide brimmed hat for outdoors work.

Other:

# USE OF PROTECTIVE CLOTHING AND EQUIPMENT

Protective clothing and equipment is provided for your protection for some hazardous tasks.  You must use these as instructed, clean these properly after use; keep them in good order.  You must let the manager know if protective equipment is damaged or not available, or if you are having difficulty in using the equipment provided.  Protective equipment includes:

  - Ear muffs or plugs where noise is a problem

  - A face mask or respirator when dust (including grain dust) is a problem, or if you suffer from asthma or other respiratory condition.

  - Sunscreen when you are working outdoors.

  - Eye protection when grain dust is a problem.

  - A helmet for head protection when riding a motorbike or quad.

# TRACTORS, HEADERS AND MACHINERY OPERATION AND MAINTENANCE

  - Before starting any machine you must undertake a safety check.  This includes checking the condition/level of fuel, oil, water, transmission fluid, tyres, brakes and guards.

  - You should report to the manager any malfunction or condition likely to affect the safe operation of the machine.  This includes guards that are damaged or missing and where there are exposed moving parts of machines causing a safety hazard.

  - When leaving a tractor or header with the engine running, you must ensure that all equipment is disengaged and the machine is in ‘PARK’.

  - Whenever you remove a guard to undertake machinery maintenance, or to clear a blockage, you must replace that guard after finishing the repair and/ or before restarting the machine.

  - Before working under any machinery, especially raised header fronts or other raised machinery, you must ensure that the machine is adequately blocked and supported.

  - Keep in mind the need to be aware of the location of overhead powerlines and operate all tall machinery well clear of all powerlines.

  - Do not get inside to clean or maintain any header grain bin with the augers engaged.

Other:

# CHASER BINS

Unguarded PTO drive shafts, pulleys, belts, chains and sweep augers are involved with workers being entangled and causing many serious hand and leg injures, including amputation.

  - Make sure all PTO drive shafts, pulleys, drive belts and augers are properly guarded and guards are always in place.

  - Do not get inside any chaser bin to clean sweep augers.  Make sure the tractor PTO is disengaged, hydraulics are neutralised, turn off the tractor motor and remove the key.

  - Restart and use the tractor only when there are no workers inside the chaser bin.

  - Do not climb the back trucks to check emptying above grain auger hoppers while the auger is running.

# GRAIN AUGERS

Unguarded grain auger flights, drive belts, pulleys and shafts a cause of many serious injuries, especially to hands, feet and hair becoming entangled.

  - Make sure all grain augers are properly guarded and bystanders are clear before being started.

  - Empty and lower augers before being moved or transported to prevent the auger collapsing or toppling.

  - Make sure augers are not used near and are well operated well clear of overhead power lines.

  - Other:

# SILOS AND FIELD BINS

There have been many injuries when working with climbing and towing field bins, workers being engulfed by grain; falling when climbing and working on top of silos to check fill levels and closing silo lids.

Report any structural damage to silos and field bins you identify so that it can be repaired.

Do not get inside any silo or field bin unless you have been instructed and there is an observer outside.

Do not climb any silo without permission where ladder fall prevention guards are not fitted or trained and using a fall prevention harness.

  - Other:

# HYGEINE

Good personal hygiene will help to reduce the risk of illness due to infection or contamination with hazardous chemicals that your worker may be exposed to.  Your workers must:

Ensure that they wash after working and after handling pesticides or dogs or other animals, especially before eating or smoking.

Make sure that work clothes are washed regularly.  They will need to wash them daily if they’re working in areas that have been sprayed with pesticides.  Never re-wear clothes that are contaminated with pesticides.

NOT smoke inside buildings, farm vehicles or cabined machines.

Keep up to date with their tetanus vaccinations.

NOT be in possession of, consume or be suffering the effects of alcohol or any illicit drug.

# FATIGUE

There are certain times of the year when we are very busy on this farm.  At these times it is often necessary to work during the night.

You are encouraged to take frequent short breaks to reduce fatigue during these busy times.  Fatigue increases the risk of accident and injury for operators of machinery as reflex times are slowed significantly and concentration lost.

When working continuous long hours, it is important to get good sleep to prevent fatigue.  Make sure that you also eat well and drink enough water.

When working during the night it is even more important to be alert.

Let us know if you are really tired and loosing concentration so we can organise a break or swap jobs for a while.

# AMENITIES

The following amenities have been made available for your use and the use of your workers:

Toilets				…………………………………………………..

Shelter				…………………………………………………..

Drinking water		…………………………………………………..

Washing facilities		…………………………………………………..

# EMERGENCY ARRANGEMENTS

In an emergency, Dial 000 (Triple Zero) for ambulance, fire brigade  or police.

First aid kits are located

Emergency telephone numbers are located at the telephones at

The UHF/ VHF channel used on the farm is

The bush fire brigade channel is

Fire extinguishers are located

Fire blankets are located

Trained and designated First Aid officer is/ are:

# COMMUNICATION

Please supply your contact details to …………………………………………………………. in case we need to contact you in an emergency.

If you need to contact the manager of this farm is:

(Name)

Phone (daytime):

Phone (night time):

Phone (mobile):

Fax:

Email:

The people who are available to handle any questions that you have are:

| Name ………………………………. ………………………………. | Telephone ………………………………. ………………………………. | Position ………………………………. ………………………………. |
| --- | --- | --- |

# SNAKES AND SPIDERS

Snakes are found on and around the farm, especially around dams and creeks.  Many snakes are poisonous and many snake bites are a result of snakes being chased and killed.

  - If you come across a snake, move away and let the snake move away.  If other workers are nearby, let them know where the snake has gone. Don’t chase or corner them.

  - If bitten by a snake, place a firm pad over the bite, bandage securely and keep the limb as still as possible.  Use the communication system to get help quickly.

# WORKERS COMPENSATION ARRANGMENTS*

EITHER

You, the contractor, are responsible for workers compensation insurance for the workers in your team.  Please supply a Certificate of Currency from your Workers’ Compensation Insurer.

OR

Your workers are covered for workers compensation by the policy of this farm.  A copy of the policy is available for perusal, and the rights of workers and how to make a claim are

displayed at …………………………………………………..........................................

*  (Advice is available regarding who is responsible for Workers’ Compensation from your insurer, your State’s Work Health Authority, your Farmer Organization or Union).

# INJURY REPORTING

We keep records of injury or illness that results from your work and record in this in our Injury Register.  We record all injuries / illness whether minor or major.  Injury Forms are located:

…………….…………………………………………………………………………… or contact the owner/ manager.

# GENERAL

If you feel that you, or your workers, do not have the resources or experience to undertake a job safely, please advise the owner/ manager, and do not proceed with the job.

The laws of this state require that the owner/ manager provide a safe place of work and safe work systems.  In order to help us meet this responsibility, we ask you to tell the owner /manager about any safety hazard or problem that you encounter.

We ask you and your worker to cooperate with our health and safety program, and comply with our rules to protect your own safety and the safety of others.

It is not acceptable for any worker to be under the influence of alcohol or other drugs during work on this farm.  Any who is affected by alcohol or drugs will be asked to leave the farm until it is clear that no-one’s safety is at risk.

There are children on this farm.  Their safety must be a high priority.  Please be careful when driving vehicles and operating machinery; never reverse without checking for children or bystanders.

Please do not bring children on to this farm.

Please do not bring dogs on to this farm.

# OTHER ISSUES AND INFORMATION

The safety of people on this farm takes precedence over all other considerations

Signed: ____________________________	Date: ___ / ___ / ___

Contractor

Name: _____________________________

Print

Signed: ____________________________	Date: ___ / ___ / ___

Owner / Manager

Name: _____________________________

Print

###### DISCLAIMER

This document does not, in any way, excuse a person from doing all that is reasonable to ensure the health and safety of themselves and others.  Legislative requirements vary between states and territories.  Therefore, it is necessary to check with the relevant state or territory occupational health and safety authority for appropriate information.

Notes:

………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………